## Slide 1: SPHERE STANDARDS FOR WATER AND SANITATION

## Slide 2
Minimum standards
Guidance notes
Key indicators

## Slide 3: Areas of Key Standards
Hygiene Promotion
Water Supply
Excreta Disposal
Vector Control
Solid Waste Management
Drainage

## Slide 4: Hygiene Promotion
How many Hygiene Promoters for 10,000 people?

## Slide 5: Planning for water distribution

## Slide 6: Water Supply Standards
Water Quantity
Water Quality
Water Use Facilities and Goods

## Slide 7: Water Quantity
What is the maximum distance from any household to the nearest water point?
What is the maximum queuing time at a water source?
What is the minimum amount of water that needs to be provided for a mosque?

## Slide 8: Water Quantity Considerations
Climate
Accuracy of population data
Culture
Agriculture
Mud bricks and other construction

## Slide 9: People per water source
250 people per tap
500 people per handpump
400 people per single-user open well

## Slide 10: Queuing
A queuing time of more than 15 minutes indicates:
    Insufficient number of sources / taps
    Insufficient flow rate
    Insufficient access time

## Slide 11: Considerations for Installing Sources
Design pressure and distribution costs (tapstands)
Groundwater availability (wells)
Flooding
Security
Equity
Distance
Drainage

## Slide 12: Institutional Needs
Page 93

## Slide 13: Water Quality - Sanitary Survey
If the answer to any of these questions is No, there is a strong likelihood that there is an issue with water quality.

## Slide 14: Key Indicators – Water Use Facilities and Goods
What is the minimum amount of water containers per family?
What is the minimum amount of soap for personal hygiene per person per month?

## Slide 15: Planning for public sanitation

## Slide 16: Excreta Disposal Standards
Access to, and number of, toilets
Design, construction, and use of toilets

## Slide 17: How Many Latrines?
COMMUNAL TOILETS
Initial emergency phase: 1 drophole per 50 people
Provide 1 drophole per 20 people as soon as possible
Transition to family latrines if and when possible
FAMILY TOILETS
1 toilet per family
A family might be more than one house and could be up to 20 people.
Work with community to decide how many family toilets are necessary

## Slide 18: Latrine Program
Design
Quantity
Location

## Slide 19: Latrine design
Accessibility for children and disabled
Comfort and community desires
Cost
Soil type and water table
Privacy and security
Anal cleansing material (amount of water used)
Emptying/Longevity

## Slide 20: Latrine Quantity
Communal vs. family
Accuracy of population data
Culture
Land availability

## Slide 21: Latrine Location
Community preferences (not just leaders, not just men)
Gender division
Handwashing facilities
Flooding, drainage, water table

## Slide 22: Institutional Needs
Page 94