## Slide 1: Water and Sanitation Planning for Response
Using SPHERE

## Slide 2: WatSan Response Planning in Emergencies
How much water do people need for drinking per day?
How much water do people need per day?
How far should people walk to collect water?
What should the water quality be like?
How many latrines do people need?
How close should latrines be to houses?
How far away should a camp be to a mosquito breeding site?
What size refuse container do a family need?

## Slide 3: SPHERE
Minimum Standards for Emergency Response
Key Indicators
Standards for quality, quantity and access
Key reference
Chapter 2 – Water and Sanitation

## Slide 4
Minimum standards
Guidance notes
Key indicators

## Slide 5: Areas of Key Standards
Hygiene Promotion
Water Supply
Excreta Disposal
Vector Control
Solid Waste Management
Drainage

## Slide 6: SPHERE – Exercise Four Groups
Group One: Water Supply
Group Two: Excreta Disposal and Hygiene Promotion
Group Three: Vector Control and Drainage
Group Four: Solid Waste Management

## Slide 7: SPHERE – Key Indicators
Water Supply
15L/person/day (3L of drinking water/person/day)
500m from water collection point
Takes no more than 3min to fill a 20L container
0 faecal coliforms/100ml
0.5mg/L free chlorine at the tap
2 containers of 10-20L per household

## Slide 8: SPHERE – Key Indicators
Sanitation and hygiene promotion
1 latrine for every 20 people (or 50 in emergencies)
Latrines less than 50m from houses
Community included in the design and siting of latrines
Hand washing facilities located next to latrines
Gender considerations for latrines

## Slide 9: SPHERE – Key Indicators
Vector Control and drainage
All populations understand the modes of transmission
People avoid exposure to mosquitoes during peak biting times
People with malaria are diagnosed and receive treatment
Personnel carrying out chemical vector control measures are protected
Water points are kept free from standing water

## Slide 10: SPHERE – Key Indicators
Solid waste Management
Household waste is put in containers for daily collection, burnt or buried
All households are no more than 100m from a refuse pit
At least one 100L refuse container is available per 10 families