## Slide 1: Cholera & Oral Rehydration Therapy Training Level 2 – Emergency ORP operators Session #02a – Setting up an Emergency ORP and a referral system
Date, Place
Notes: Register participants
Official opening and recitals

## Slide 2: Session overview
What is an ORP
When to set up an ORP ?
Activities of an ORP
Treatment Capacity
ORP kit contents

## Slide 3: ORP = Oral rehydration point
Notes: SHOW the ORP kit and how it works

## Slide 4: What is an ORP?
An ORP is a point of entry, at community level, to AWD / cholera treatment and referral - able to handle a significant number of suspected cholera / AWD patients.
The RCRC has created an ORP kit that contains all materials necessary for one or several ORP volunteers to successfully provide these services at community level

## Slide 5: What is an ORP ?
Contrary to the ORT volunteer system (available at all times), an ORP is meant to be deployed temporarily during a AWD/Cholera outbreak (emergency response)
It is a visible structure in a clearly defined area that is open 12 hours a day, and where security permits and cases require, up to 24 hours a day
It is more operational with access to treated water, sanitation and a strong Infection Prevention and Control (IPC) element
It is manned by a minimum of 2 volunteers, preferably 4 (on rotation)

## Slide 6: When to set up an ORP ?
An ORP should be deployed during an AWD/Cholera outbreak (emergency response)
When a significant number of cases are reported in or around a community and is too many for the ORT volunteer to deal with (> 05-10 cases/day)
In partnership and agreement with the Local Health Authorities
The ORP will be closed when the number of AWD cases goes down.

## Slide 7: This is an ORP

## Slide 8: …and so is this

## Slide 9: ORPs as first level of care
Cholera Treatment Center
Cholera Treatment Unit
Oral Rehydration Point in the community

## Slide 10: Activities of an ORP
Initiate early treatment of mild to moderate cases of dehydration by giving ORS
Provide an infection free environment through strict IPC procedures
Distribute key supplies such as ORS, soap and household water treatment chemicals or advice
Act as a referral point for severe, or at-risk cases to health facilities
Be part of community-based surveillance by recording all suspected cases of cholera
Provide key health and hygiene messages to the community to help prevent cholera.
Key point for social mobilization activities in the community

## Slide 11: Number of people treated
The kit can produce enough water to treat approximately 35 patients per day using the safe water from the filter
You should not see more than 25-30 people per day, if you do, alert your ORP supervisor

## Slide 12: What is needed for an ORP?
ORP kit
ORP operators
ORP
ORP site
Referral plan

## Slide 13: Contents of the ORP Kit
Key Contents
Water filter
Sanitation platform
Tarpaulins and rope
Foldable chairs and table
Buckets (with and without taps) and cleaning gear
1 and 0.5 litre jugs, cups, spoons and washing up bowl
Stationary: patient log, notebooks and pens, laminated reference cards, labelling materials.
Consumables: ORS, sugar and salt, (zinc tablets), water treatment chemicals, soap, chlorine
Visibility, protective gear and demarcation: aprons, bibs, flags and demarcation tape
NB. Other protective gear will be provided separately from the kit due to sizing

## Slide 14: Contents of the ORP kit

## Slide 15: ORP kit Contents: Water Filter
Two 20 -litre containers that stack on top of one another.
The first contains two ceramic filters that provide clean water using gravity filtration
  The filters stop 99% of all bacteria and viruses (germs)
They produce 2 litres of water per hour
They provide clean safe water without having to add chemicals:
  Better acceptability
  Better taste of ORS
  ORP has enough clean and safe water at all times
Notes: Note that other filters may be tried in different areas

## Slide 16: ORP Kit Contents: Water Filter
Ceramic filter candle
Water passes from the outside of the candle to the inside, leaving particles of dirt, bacteria, etc. on the outside of the ceramic.
The filtered water then passes out of the candle through the mount.

## Slide 17: ORP Kit Contents: Sanitation Platform

## Slide 18: ORP Kit Contents: Tarpaulins
Use for shelter from rain or sun with use of rope.
Use for IPC. Tarpaulin is easy to clean and so may be used as a ground sheet on which the patients sit.
Use for the superstructure of a latrine
To cover benches or chairs preventing contamination of furniture from community

## Slide 19: ORP Kit Contents: Furniture
The kit will contain basic furniture: two chairs and a table.
A NS may choose to add items of furniture to the basic kit or furniture may have to be provided by the community
Bare in mind that furniture may become stigmatized or damaged
Borrowed furniture may be protected using tarpaulins

## Slide 20: ORP Kit Contents: Buckets
Buckets will have different purposes. The kit contains some buckets with taps and others without.
Buckets will be used to mix different chlorine solutions; for handwashing points; for cleaning; and will also be given to patients if they need to vomit or cannot get to the toilet.
All buckets should be clearly labelled in terms of purpose or indicating the type of chlorine solution contained

## Slide 21: ORP Kit Contents: Plastics
Plastics will get broken so keep a record of how many jugs and cups are useable.
Do not allow patients that are referred or that are going home to leave with cups. Mixed ORS should be put in bottles
Ensure there is a system in place so that it is clear which jugs/cups are clean and which are dirty

## Slide 22: ORP Kit Contents: Stationary
A log book for the documenting of cases will be provided and should be strictly kept.
Labelling stationary and signs will be provided for buckets, but also to guide patient flow along with sticky tape.
Laminated reference/cheat cards will be provided which are to help volunteers who may have forgotten parts of their training.

## Slide 23: ORP Kit Contents: Consumables
ORS and chlorine will be distributed to the ORP volunteers separately
Remember to inform your ORP supervisor if you are running low on any of these items

## Slide 24: ORP Kit Contents: Visibility, Protective Gear and Demarcation
Aprons, bibs and flags will be provided for both visibility and protection purposes
Note that personal protective gear will be provided separately to each volunteer due to sizing
Demarcation tape is included which should be used to define the area of the ORP and also to indicate patient control and flow.

## Slide 25: ORPs in an Urban Context: OR Corners
Urban
Safe water more likely to be available nearby
Health facilities more likely to be nearby
Households more densely situated
Rural
Safe water less available
Distant Health centers
Scattered households

## Slide 26: Activity
Prepare your ORP deployment.
Make a list of all items needed to be ready to operate tomorrow morning.
Look at what is already present in the ORP kit and list additional items you would need to procure either from the community or the Red Cross.

## Slide 27: Summary