PRACTICAL  FORM

JAR TEST

AIM: To learn how to carry out a jar test

TIME: 1 hour

PARTICIPANTS: One group of 5 participants carries out the practical and the rest of the course observes.

MATERIAL:

10 litres of raw water

7 plastic jars (1 litre)

1 litre of clean water

1 scale

1 watch

1 spoon

1 turbidimetre

500 gr. of Aluminium Sulphate

HANDOUTS:

- Jar test summary

- Jar test procedure

LOCATION: The same classroom as for the presentations.

PRACTICAL DESCRIPTION:

This practical takes place after the presentation “Flocculation and Chlorine control. Jar test”. One group of 5 participants carries out the practical in front of the course.

The practical takes place following the handout “Jar test procedure”. Once the first part of the practical has concluded, and during the 30 minute sedimentation time, the facilitator provides the presentation “Water treatment processes”.

We check the results of the test alter the presentation. Each participant records the data in the table included in the provided handout. The facilitator discusses the validity of the results with the participants.