SESSION FORM

WATER TREATMENT PLANT SETA

AIMS:

a) To install and to correctly operate the water treatment plant (WTP) SETA.

b) To carry out the backwashing and washing of the filters of the WTP SETA.

c) To make the chemical solutions used by the WTP SETA.

d) To produce drinking water with the WTP SETA.

e) To analyse the water produced by the WTP SETA.

f)  To install the flexible water tank and the water horse of the WTP SETA.

TIME: 5 hours

CONTENTS:

Activity a) Presentation: “Water treatment plant SETA” (50 min.)

Activity b) Practical: Installation and levelling of the WTP SETA (15 min)

Activity c) Practical: Practical knowledge of the WTP SETA (30 min.)

Activity d) Practical: Starting and stopping the plant. Backwashing and washing of the filters of

the WTP SETA (60 min.)

Activity e) Practical: Installation of the 10,000 litre flexible bladder tanks and water horse of the

WTP SETA (15 min)

Activity f) Practical: Preparation of the Chlorine and Aluminium Sulphate solutions (30 min)

Activity g) Practical: Drinking water production, water analysis and filling up the flexible bladder

tank.

HANDOUTS:

- WTP Manual Mod.2E 3000 SETA (PRACTICAL)

- WTP SETA Technical information (PRACTICAL)

- Field Log Book (1 per 5 participants) (PRACTICAL)