PRACTICAL FORM

WALL SPRAYING

AIMS:

- To prepare an insecticide solution (deltamethrin, lambdacihalothrin, etc)

- To practice the wall spraying technique

TIME: 50 min

PARTICIPANTS: The course is divided into 5 groups.

MATERIALS:

Water

Box SP/ERU/WATSAN/SAN/PUL/ 01

White tape or chalk

5 buckets (10 litres)

Scale

Funnel

Stopwatch

HANDOUTS:

None

LOCATION:  Three outdoor walls with dimensions 7m x 3 m.

PRACTICAL DESCRIPTION:

Activity a)  Preparation in a 10 litre bucket of a deltamethrin or lambdacihalothrin solution after

carrying out the necessary calculations. Use the handout.

Activity b) To practice wall spraying using water only. Use the manually-operated backpack

sprayers. The spraying ratio is 19 m2 per min.

The 5 groups of the course rotate among both activities. Each group member practices the wall spraying technique.

CALCULATIONS (see Vector Control Methods used by individuals and communities. WHO. Chapter 9 House-spraying with residual insecticides pg. 362):

*  If the standard spraying procedure is adopted the spray liquid will be applied at a rate of 40 ml per m2 o 1 litre per 25 m2. This amount of suspension normally stays on the surface without run-off.

Water-dispersible powder.

One litre of spray suspension can be prepared using the following formula:

WALL SPRAYING (see Vector Control Methods used by individuals and communities. WHO. Chapter 9 House-spraying with residual insecticides pg. 376):

PHOTO:

# Text boxes

Spraying process in a village.

It can be observed that, erroneously, the workers do not wear protective equipment (masks, goggles and gloves).